## Slide 1: Out of Order Execution (OoO)

## Slide 3: Tomasulo Organization
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 4: Reservation Station Components
Op: Operation to perform in the unit (e.g., + or –)
Vj, Vk: Value of Source operands
  Store buffers has V field, result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
  Note: No ready flags as in Scoreboard; Qj,Qk=0 => ready
  Store buffers only have Qi for RS producing result
Busy: Indicates reservation station or FU is busy
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 5: Three Stages of Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues instr & sends operands (renames registers).
2. Execute—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available
Normal data bus: data + destination (“go to” bus)
Common data bus: data + source (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast

## Slide 6: Tomasulo Example

## Slide 7: Tomasulo Example Cycle 1

## Slide 8: Tomasulo Example Cycle 2
Note: Unlike 6600, can have multiple loads outstanding
(This was not an inherent limitation of scoreboarding)

## Slide 9: Tomasulo Example Cycle 3
Note: registers names are removed (“renamed”) in Reservation Stations; MULT issued vs. scoreboard
Load1 completing; what is waiting for Load1?

## Slide 10: Tomasulo Example Cycle 4
Load2 completing; what is waiting for Load1?

## Slide 11: Tomasulo Example Cycle 5

## Slide 12: Tomasulo Example Cycle 6
Issue ADDD here vs. scoreboard?

## Slide 13: Tomasulo Example Cycle 7
Add1 completing; what is waiting for it?

## Slide 14: Tomasulo Example Cycle 8

## Slide 15: Tomasulo Example Cycle 9

## Slide 16: Tomasulo Example Cycle 10
Add2 completing; what is waiting for it?

## Slide 17: Tomasulo Example Cycle 11
Write result of ADDD here vs. scoreboard?
All quick instructions complete in this cycle!

## Slide 18: Tomasulo Example Cycle 12

## Slide 19: Tomasulo Example Cycle 13

## Slide 20: Tomasulo Example Cycle 14

## Slide 21: Tomasulo Example Cycle 15

## Slide 22: Tomasulo Example Cycle 16

## Slide 23: Faster than light computation (skip a couple of cycles)

## Slide 24: Tomasulo Example Cycle 55

## Slide 25: Tomasulo Example Cycle 56
Mult2 is completing; what is waiting for it?

## Slide 26: Tomasulo Example Cycle 57
Once again: In-order issue, out-of-order execution and completion.

## Slide 27: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, IBM 620?
Many associative stores (CDB) at high speed
Performance limited by Common Data Bus
  Each CDB must go to multiple functional units high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
    Multiple CDBs  more FU logic for parallel assoc stores
Non-precise interrupts!
  We will address this later

## Slide 28: Tomasulo Loop Example
Loop: LD F0 0 R1
MULTD F4 F0 F2
SD F4 0 R1
SUBI R1 R1 #8
BNEZ R1 Loop
Assume Multiply takes 4 clocks
Assume first load takes 8 clocks (cache miss), second load takes 1 clock (hit)
To be clear, will show clocks for SUBI, BNEZ
Reality: integer instructions ahead

## Slide 29: Loop Example

## Slide 30: Loop Example Cycle 1

## Slide 31: Loop Example Cycle 2

## Slide 32: Loop Example Cycle 3
Implicit renaming sets up “DataFlow” graph

## Slide 33: Loop Example Cycle 4
Dispatching SUBI Instruction

## Slide 34: Loop Example Cycle 5
And, BNEZ instruction

## Slide 35: Loop Example Cycle 6
Notice that F0 never sees Load from location 80

## Slide 36: Loop Example Cycle 7
Register file completely detached from computation
First and Second iteration completely overlapped

## Slide 37: Loop Example Cycle 8

## Slide 38: Loop Example Cycle 9
Load1 completing: who is waiting?
Note: Dispatching SUBI

## Slide 39: Loop Example Cycle 10
Load2 completing: who is waiting?
Note: Dispatching BNEZ

## Slide 40: Loop Example Cycle 11
Next load in sequence

## Slide 41: Loop Example Cycle 12
Why not issue third multiply?

## Slide 42: Loop Example Cycle 13

## Slide 43: Loop Example Cycle 14
Mult1 completing. Who is waiting?

## Slide 44: Loop Example Cycle 15
Mult2 completing. Who is waiting?

## Slide 45: Loop Example Cycle 16

## Slide 46: Loop Example Cycle 17

## Slide 47: Loop Example Cycle 18

## Slide 48: Loop Example Cycle 19

## Slide 49: Loop Example Cycle 20