## Slide 1: Exploiting Instruction Level Parallelism with Software Approaches
Compiler Techniques for Exposing ILP

## Slide 2
How compilers can help processors ?

## Slide 3: Limited ILP
Chain of dependencies
ADD R1, R2, R3
ADD R4, R1, R5
ADD R7, R4, R8
ADD R10, R7, R3
ADD R11, R10, R12

## Slide 4: Limited Window
Independent instructions far apart
  Ideal processor
    No problem
  Real processor
    Some instructions can never be seen
      Runs out of ROB space
      Runs out of reservation stations
  Example:

## Slide 5: Tree Height Reduction
R8=R2+R3+R4+R5
R8=(R2+R3)+(R4+R5)
ADD R8, R2, R3
ADD R8, R8, R4
ADD R8, R8, R5
ADD R8, R2, R3
ADD R7, R4, R5
ADD R8, R8, R7

## Slide 6: Tree Height Reduction
R8=R2+R3+R4+R5
R8=(R2+R3)+(R4+R5)
ADD R8, R2, R3
ADD R8, R8, R4
ADD R8, R8, R5
ADD R8, R2, R3
ADD R7, R4, R5
ADD R8, R8, R7
Independent instructions can execute in parallel on a processor that can do at least 2 instruction per cycles

## Slide 7: Tree Height Reduction
Associativity
  Not all operations are associative
  We can only apply tree height reduction if the final result is the same as if we did things in proper order

## Slide 8: Example
ADD R10, R1, R2 | 
SUB R10, R10, R3 | 
ADD R10, R10, R4 | 
SUB R10, R10, R5 | 
ADD R10, R10, R6 | 
SUB R10, R10, R7 | 

## Slide 9: Example
What we are trying to compute (Rewrite the expression)
  R1+R2-R3+R4-R5+R6-R7
Rewrite the expression
  R1+R2
  R4+R6
  (R1+R2)+(R4+R6)
  R3+R5
  (R3+R5)+R7
  ((R1+R2) +(R4+R6))-((R3+R5)+R7)

## Slide 10: Example
ADD R10, R1, R2 | ADD R10, R1, R2
SUB R10, R10, R3 | ADD R11, R4, R6
ADD R10, R10, R4 | ADD R10, R10, R11
SUB R10, R10, R5 | ADD R11, R3, R5
ADD R10, R10, R6 | ADD R11, R11, R7
SUB R10, R10, R7 | SUB R10, R10, R11
ILP
ILP

## Slide 11: Instruction Scheduling
Techniques that make independent instructions easily available to the processor
Ideal Processor
  Able to look at infinite number of instructions
Real Processor
  Able to see only a limited number of instructions
Take help of the compiler

## Slide 12: Instruction Scheduling
Instruction Scheduling
  Independent instructions
Dynamic Scheduling
  Tomosula’s algorithm : Hardware based approach
Static Scheduling
  Compiler based approach

## Slide 13: Example
LW R2, 0(R1) | 
ADD R2, R2, R0 | 
SW R2, 0(R1) | 
ADDI R1, R1,4 | 
BNE R1, R3, loop | 
Load 2 cycles
Add takes 3 cycles
A very simple Processor only looks at the next instruction (single issue), in-order, no reservation stations

## Slide 14: Example
LW R2, 0(R1) | LW R2, 0(R1)
ADD R2, R2, R0 | 1 stall
SW R2, 0(R1) | ADD R2, R2, R0
ADDI R1, R1,4 | 2 stall
BNE R1, R3, loop | SW R2, 0(R1)
 | ADDI R1, R1,4
 | 2 stall
 | BNE R1, R3, loop

## Slide 15: Example
LW R2, 0(R1) | LW R2, 0(R1)
1 stall | ADDI R1, R1, 4
ADD R2, R2, R0 | ADD R2, R2, R0
2 stall | 2 stall
SW R2, 0(R1) | SW R2, 0(R1)
ADDI R1, R1,4 | ADDI R1, R1,4
2 stall | 2 stall
BNE R1, R3, loop | BNE R1, R3, loop

## Slide 16: Example
LW R2, 0(R1) | LW R2, 0(R1)
1 stall | ADDI R1, R1, 4
ADD R2, R2, R0 | ADD R2, R2, R0
2 stall | 2 stall
SW R2, 0(R1) | SW R2, 0(R1)
ADDI R1, R1,4 | ADDI R1, R1,4
2 stall | 2 stall
BNE R1, R3, loop | BNE R1, R3, loop

## Slide 17: Example
LW R2, 0(R1) | LW R2, 0(R1)
1 stall | 
ADD R2, R2, R0 | 
2 stall | 
SW R2, 0(R1) | 
ADDI R1, R1,4 | 
2 stall | 
BNE R1, R3, loop | 

## Slide 18: Instruction Scheduling
Find Independent Instructions that can be used to replace the stalls

## Slide 19: Instruction Scheduling
LW R1, 0(R2) | 
ADD R1, R1, R3 | 
SW R1, 0(R2) | 
LW R1, 0(R4) | 
ADD R1, R1, R5 | 
SW R1, 0(R4) | 
Load 2 cycles
Add takes 1cycle
Store 1 Cycle
-One Instruction per cycle
-In order

## Slide 20: Instruction Scheduling
LW R1, 0(R2) | LW R1, 0(R2)
ADD R1, R1, R3 | LW R10, 0(R4)
SW R1, 0(R2) | ADD R1, R1, R3
LW R1, 0(R4) | ADD R10, R10, R5
ADD R1, R1, R5 | SW R1, 0(R2)
SW R1, 0(R4) | SW R10, 0(R4)
Load 2 cycles
Add takes 1cycle
Store 1 Cycle
-One Instruction per cycle
-In order
Cycles
Cycles

## Slide 21: Loop Unrolling
For (i=1000; i !=0; i--)
a[i]=a[i]+5;

## Slide 24: Loop Unrolling
By making each iteration of the new loop do more than one iteration of the old loop
  Each iteration of the new loop would do the work it should be doing plus the work of the next iteration

## Slide 25: Loop Unrolling
For (i=1000; i !=0; i--)
a[i]=a[i]+5;
a[i]=a[i]+5;

## Slide 26: Loop Unrolling
For (i=1000; i !=0; i=i-2)
a[i]=a[i]+5;
a[i-1]=a[i-1]+5;

## Slide 27: Super Scalar Processor

## Slide 28
Assumptions
Load: 2-cycles (1 cycle stall for consumer)
FP ALU: 4-cycles (3 cycle stall for consumer; 2 cycle stall
if the consumer is a store)
One branch delay slot
Int ALU: 1-cycle (no stall for consumer, 1 cycle stall if the
consumer is a branch)
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 29
Loop Example
for (i=1000; i>0; i--)
x[i] = x[i] + s;
Loop: L.D F0, 0(R1) ; F0 = array element
ADD.D F4, F0, F2 ; add scalar
S.D F4, 0(R1) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
BNE R1, R2, Loop ; branch if R1 != R2
NOP
Source code
Assembly code

## Slide 30
Loop Example
for (i=1000; i>0; i--)
x[i] = x[i] + s;
Loop: L.D F0, 0(R1) ; F0 = array element
ADD.D F4, F0, F2 ; add scalar
S.D F4, 0(R1) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
BNE R1, R2, Loop ; branch if R1 != R2
NOP
Source code
Assembly code
Loop: L.D F0, 0(R1) ; F0 = array element
stall
ADD.D F4, F0, F2 ; add scalar
stall
stall
S.D F4, 0(R1) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
stall
BNE R1, R2, Loop ; branch if R1 != R2
stall
10-cycle
schedule
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 31
Smart Schedule
By re-ordering instructions, it takes 6 cycles per iteration instead of 10
We were able to violate an anti-dependence easily because an
immediate was involved
Loop overhead (instrs that do book-keeping for the loop): 2
Actual work (the ld, add.d, and s.d): 3 instrs
Can we somehow get execution time to be 3 cycles per iteration?
Loop: L.D F0, 0(R1)
stall
ADD.D F4, F0, F2
stall
stall
S.D F4, 0(R1)
DADDUI R1, R1,# -8
stall
BNE R1, R2, Loop
stall
Loop: L.D F0, 0(R1)
DADDUI R1, R1,# -8
ADD.D F4, F0, F2
stall
BNE R1, R2, Loop
S.D F4, 8(R1)
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 32
Loop Unrolling
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
L.D F6, -8(R1)
ADD.D F8, F6, F2
S.D F8, -8(R1)
L.D F10,-16(R1)
ADD.D F12, F10, F2
S.D F12, -16(R1)
L.D F14, -24(R1)
ADD.D F16, F14, F2
S.D F16, -24(R1)
DADDUI R1, R1, #-32
BNE R1,R2, Loop
Loop overhead: 2 instrs; Work: 12 instrs
How long will the above schedule take to complete?

## Slide 33
Scheduled and Unrolled Loop
Loop: L.D F0, 0(R1)
L.D F6, -8(R1)
L.D F10,-16(R1)
L.D F14, -24(R1)
ADD.D F4, F0, F2
ADD.D F8, F6, F2
ADD.D F12, F10, F2
ADD.D F16, F14, F2
S.D F4, 0(R1)
S.D F8, -8(R1)
DADDUI R1, R1, # -32
S.D F12, 16(R1)
BNE R1,R2, Loop
S.D F16, 8(R1)
Execution time: 14 cycles or 3.5 cycles per original iteration
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 34
Superscalar Pipelines
Integer pipeline FP pipeline
Loop: L.D F0,0(R1)
L.D F6,-8(R1)
L.D F10,-16(R1) ADD.D F4,F0,F2
L.D F14,-24(R1) ADD.D F8,F6,F2
L.D F18,-32(R1) ADD.D F12,F10,F2
S.D F4,0(R1) ADD.D F16,F14,F2
S.D F8,-8(R1) ADD.D F20,F18,F2
S.D F12,-16(R1)
DADDUI R1,R1,# -40
S.D F16,16(R1)
BNE R1,R2,Loop
S.D F20,8(R1)
Need unroll by degree 5 to eliminate stalls
The compiler may specify instructions that can be issued as one packet
The compiler may specify a fixed number of instructions in each packet:
Very Large Instruction Word (VLIW)

## Slide 35: Loop Unrolling
Loop: LW R1, 0(R2)
After scheduling the loop (w/o unrolling)
  ________________cycles/1000 iterations
After unrolling once and scheduling
  ________________cycles/1000 iterations
Loop: LW R1, 0(R2)
ADD R3, R3, R1
ADDI R2, R2, 4
BNE R2, R4, Loop
In Order: 1 Instruction per Cycle
LD -> any : 2 stall
ADD/ADDI -> any: 1 stalls

## Slide 36: Loop Unrolling
It reduces the overall number of instructions we have to execute
It also can reduce the IPC/CPI in addition to reducing the number of instructions

## Slide 37
Loop Unrolling
Increases program size
Requires more registers
To unroll an n-iteration loop by degree k, we will need (n/k)
iterations of the larger loop, followed by (n mod k) iterations
of the original loop

## Slide 38: Function Call In lining
Optimization
Avoid the overhead of calling the function and returning from it
  Prepare function parameters
  Call function
  Return from the function
Simply take the work of the parameter and put it there

## Slide 39: Function Call In lining
Instructions
Prepare function parameters
Call function
Other instructions
Function Rd, Rs1, Rs2
Return

## Slide 40: Function Call In lining
Instructions
Add Rd1, Rs1, Rs2
Other instructions
Eliminates call/return overheads
Helps in Scheduling (imp)

## Slide 41: Function Call Inline (Disadvantages)
Code Bloat
  For large codes

## Slide 42: Example (Function In lining) scheduling and over head
LW A0, 0(R1) | 
CALL ADDSQUARE | 
 | ADDSQUARE:
 | MUL A0, A0, A0
 | ADD RV, A0, A1
 | RETURN
SW RV, 0(R2) | 
LW 2 CYCLES
CALL 2 CYCLES
RETURN 2 CYCLES
SW/ADD 1 CYCLE
MUL 3 CYCLES

## Slide 43: Example (Function In lining) scheduling and over head
LW A0, 0(R1) | 
MUL A0, A0, A0 | 
ADD RV, A0, A1 | 
SW RV, 0(R2) | 
LW 2 CYCLES
CALL 2 CYCLES
RETURN 2 CYCLES
SW/ADD 1 CYCLE
MUL 3 CYCLES

## Slide 45
Software Pipeline?!
L.D
ADD.D
S.D
DADDUI
BNE
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
L.D
ADD.D
DADDUI
BNE
DADDUI
BNE
DADDUI
BNE
DADDUI
BNE
DADDUI
BNE
…
…
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop

## Slide 46
Software Pipeline?!
L.D
ADD.D
S.D
DADDUI
BNE
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
L.D
ADD.D
DADDUI
BNE
DADDUI
BNE
DADDUI
BNE
DADDUI
BNE
DADDUI
BNE
…
…
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
Store for Iter. 1, Add for Iter. 4 and Load for Iter. 6

## Slide 47
Software Pipeline
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
L.D
Original iter 1
Original iter 2
Original iter 3
Original iter 4
New iter 1
New iter 2
New iter 3
New iter 4

## Slide 48
Software Pipelining
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
Loop: S.D F4, 16(R1)
ADD.D F4, F0, F2
L.D F0, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
Advantages: achieves nearly the same effect as loop unrolling, but
without the code expansion – an unrolled loop may have inefficiencies
at the start and end of each iteration, while a sw-pipelined loop is
almost always in steady state – a sw-pipelined loop can also be unrolled
to reduce loop overhead
Disadvantages: does not reduce loop overhead, may require more
registers