## Slide 1: Predictions
Dr. Farhan Hussain

## Slide 2: Pipeline and Branches
Branch
  BEQ R1, R2, Label
    If (R1!=R2) just PC++
    If (R1==R2) then PC+4+Offset
Resolved in 3rd stage or can be resolved in 2nd stage
Fecth | Dedcode | ALU | MEM | WR
BEQ |  |  |  | 
 | BEQ |  |  | 
 |  | BEQ |  | 

## Slide 3: Branch Prediction
We only know PC of current instruction
  What is the value of PC for the next instruction to be fetched
We have to guess
  Is this a branch instruction?
  Is it taken?
  If taken, what is the target PC?

## Slide 4: Branch Prediction
We only know PC of current instruction
  What is the value of PC for the next instruction to be fetched
We have to guess
  Is this a branch instruction?
  Is it taken?
  If taken, what is the target PC?
Is this a taken branch
Actually Boils down to a single decision

## Slide 5: Branch Prediction Accuracy
CPI=1+ Misprediction/Instructions × Penalty/Misprediction
Generally, 20% of all Instructions are branches
ACCURACY | BRANCH RESOVED IN 3RD STAGE | BRANCH RESOVED IN 10Th STAGE
50% for branch instructions 100% for all other instructions |  | 
90% for branch instructions 100% for all other instructions |  | 

## Slide 6: Branch Prediction Accuracy
CPI=1+ Misprediction/Instructions × Penalty/Misprediction
Generally, 20% of all Instructions are branches
ACCURACY | BRANCH RESOVED IN 3RD STAGE | BRANCH RESOVED IN 10Th STAGE
50% for branch instructions 100% for all other instructions | 1+0.5×0.2×2=1.2 | 1+0.5×0.2×9=1.9
90% for branch instructions 100% for all other instructions | 1+0.1×0.2×2=1.2=1.04 | 1+0.1×0.2×9=1.18

## Slide 7: Advantages of Branch Prediction
LOOP: ADD F1, F1, -1
ADD F2, F2, F2
BNEZ F1, Loop
without predictions ?
With predictions ?

## Slide 8: Advantages of Branch Prediction
LOOP: ADD F1, F1, -1 2 1
ADD F2, F2, F2 2 1
BNEZ F1, Loop 3 1
without predictions ? 7
With predictions ? 3

## Slide 9: Prediction: Branches Always not Taken
No prediction at all
  Branch would take 3 cycles or 2 cycles
  Non branch would take 2 cycles
Always using not taken prediction
  Branch would take 1 or 3 cycle
  Non branch would always take one cycle

## Slide 10: Not Taken Prediction
Simplest predictor possible
Just increment PC (No memory required no Extra hardware)
Accuracy
Almost 88 % (How: 20% of the instructions are branches and 60% of them are taken)

## Slide 11: Multiple Predictions
BNE R1, R4, Label A
BNE R1, R3, Label B
A
B
C
Label A
X
Y
Label B:
z
Fetch | Decode | ALU | MEM | WR
Branch Resolved
Using Not-taken predicator (but both branches are taken) how many cycles are wasted on misprediction until we get to Y

## Slide 12: Analysis of Branch Prediction
 | Not Taken (88%) | 99% Predictor | Speedup
5 Stage pipeline (branch resolved in 3rd stage) |  |  | 
14-stage pipeline (branch resolved in 11th stage) |  |  | 
14-stage pipeline (branch resolved in 11th stage) 4-instructions per cycle |  |  | 

## Slide 13: Analysis of Branch Prediction
 | Not Taken (88%) | 99% Predictor | Speedup
5 Stage pipeline (branch resolved in 3rd stage) | 1+0.12*2=1.24 | 1+0.01*2=1.02 | 1.21
14-stage pipeline (branch resolved in 11th stage) | 1+0.12*10=2.2 | 1+0.01*10=1.1 | 2
14-stage pipeline (branch resolved in 11th stage) 4-instructions per cycle | 0.25+0.12*10=1.45 | 0.25+0.001*10=0.35 | 4.14

## Slide 14: Cost of Misprediction in terms of Instruction wasted
05 stage pipeline with branches resolved in 3rd stage
05 stage pipeline with branches resolved in 2nd stage
14 stage pipeline with branches resolved in 11th stage
Superscalar processor with 4 instructions per cycle with branches resolved in 11th cycle

## Slide 15: Some Pentium 4 Processor
Fetch -------------29th stage, branch resolved in 30th cycle, ………..
Utilizes branch prediction
Multiple instructions /cycle
20% of the instructions are branches
1% of branches are mis predicted
Actual CPI is 0.5
What is the perfect CPI

## Slide 16: Branch Target Buffers

## Slide 17: Branch History Tables

## Slide 18: Branch Target Buffers
BTB has 11024 entries (0,1,2,3,….1024)
Fixed size 4-byte instructions, word aligned (0,4,8,12,16,….)
32-bit address
Which BTB entry is used for PC=0x0000AB0C

## Slide 19: Branch Prediction
Static Predictors
Dynamic Predictors
History predictors
Correlator predictors
Tournament predictors

## Slide 20: Branch Target Buffer & Branch History Table
0xC000 | Mov r2,100 |  |  | 
0xC004 | Mov R1, 0 |  |  | 
0xC008 | Loop: Beq R1,r2, done |  |  | 
0xC00C | ADD R4, R3, R1 |  |  | 
0xC010 | LW R4, 0(R4) |  |  | 
0xC014 | ADD R5, R5, R4 |  |  | 
0xC01C | ADD R1, R1, ` |  |  | 
0xC020 | J loop |  |  | 

## Slide 21: Branch Target Buffer & Branch History Table
BHT=16 entries, perfect prediction
BTB=4, entries, perfect prediction
How many times we access the BHT for each instruction
Which BHT entry do we access for each instruction
How many times we access the BTB for each instruction
Which BTB entry we access for each instruction

## Slide 22: Static Branch Prediction
Assume that a branch is always
  TAKEN
  OR
  NOT TAKEN

## Slide 23: One Bit Prediction

## Slide 24: Two Bit Prediction

## Slide 25: One Bit Prediction Vs. Two Bit Prediction
Predictor | Branch outcome | Mis prediction
 | T | 
 | T | 
 | T | 
 | N | 
 | T | 
 | N | 
 | T | 
 | T | 
 | T | 
 | N | 
 | T | 
 | N | 
 | T | 
 | T | 
 | T | 
 | N | 
 | T | 
 | N | 

## Slide 26: One Bit Prediction Vs. Two Bit Prediction
Predictor | Branch outcome | Mis prediction
 | T | 
 | T | 
 | T | 
 | N | 
 | T | 
 | N | 
 | T | 
 | T | 
 | T | 
 | N | 
 | T | 
 | N | 
 | T | 
 | T | 
 | T | 
 | N | 
 | T | 
 | N | 

## Slide 27: Correlating Branch Predictors
Is it a branch instruction
Branch Decision
  Taken
  Not Taken
If taken, What is the branch Target
If not taken (simple PC++)

## Slide 28: Correlating Branch Predictors
if (aa==2)
aa=0;
if (bb==2)
bb=0;
if (aa!=bb) {
DADDIU R3,R1,#–2
BNEZ R3,L1 ;branch b1 (aa!=2)
DADD R1,R0,R0 ;aa=0
L1: DADDIU R3,R2,#–2
BNEZ R3,L2 ;branch b2 (bb!=2)
DADD R2,R0,R0 ;bb=0
L2: DSUBU R3,R1,R2 ;R3=aa-bb
BEQZ R3,L3 ;branch b3 (aa==bb)

## Slide 29: Correlating Branch Predictors
if ( d==0 )
d = 1;
if ( d==1 )
…
BNEZ R1, L1 !branch b1
DADDIU R1, R0, #1
L1: DADDIU R3, R1, #-1
BNEZ R3, L2 !branch b2
…
L2:

## Slide 30: Correlating Branch Predictors
Initial Value of d | d==0? | b1 | Value of d before b2 | d==1? | b2
0 | yes | Not taken | 1 | yes | Not taken
1 | no | Taken | 1 | yes | Not taken
2 | no | Taken | 2 | no | Taken

## Slide 31: Correlating Branch Predictors
d=? | b1 prediction | b1 action | New b1 prediction | B2 prediction | B2 action | New b2 prediction
2 | NT | T | T | NT | T | T
0 | T | NT | NT | T | NT | NT
2 | NT | T | T | NT | T | T
0 | T | NT | NT | T | NT | NT

## Slide 32: Correlating Branch Predictors
Prediction Bits | Prediction if last branch is taken | Prediction if last branch is not taken
NT/NT | NT | NT
NT/T | NT | T
T/NT | T | NT
T/T | T | T

## Slide 33: Correlating Branch Predictors
d=? | b1 prediction | b1 action | New b1 prediction | B2 prediction | B2 action | New b2 prediction
2 | NT/NT | T | T/NT | NT/NT | T | NT/T
0 | T/NT | NT | T/NT | NT/T | NT | NT/T
2 | T/NT | T | T/NT | NT/T | T | NT/T
0 | T/NT | NT | T/NT | NT/T | NT | NT/T

## Slide 34: Hardware

## Slide 35: Tournament Predictors