## Slide 1: Large & Fast: Exploiting Memory Hierarchy
Computer Organization & Design
David A. Patterson
John L. Hennessy
Dr. Farhan Hussain

## Slide 2: Memory Hierarchy

## Slide 3: Memory Hierarchy

## Slide 4: Memory Hierarchy

## Slide 5: Memory Technologies

## Slide 6: How a Cache Works

## Slide 7: How a Cache Works

## Slide 8: HINT
Temporal Locality
Spatial Locality

## Slide 9: A Cache

## Slide 21: Example
How many total bits are required for a direct-mapped cache with 16 KB of data and 4-word blocks, assuming a 32-bit address?

## Slide 22: Example
Consider a cache with 64 blocks and a block size of 16 bytes. To what block number does byte address 1200 map?

## Slide 24: Direct Mapped Cache
Where a block can be placed in exactly one location.
There is a direct mapping from any block address in memory to a single location in the upper level of the hierarchy.

## Slide 25: Fully Associative Cache
A cache structure in which a block can be placed in any location in the cache.

## Slide 26: Set-Associative Cache
A cache that has a fixed number of locations
(at least two) where each block can be placed.

## Slide 27: Example
Placement of block 12 in a cache with eight blocks total, according to the three block placement policies.

## Slide 28
MIPS gives each program its own 32 bit address space
Programs can access any byte in their 32 bit address space
What if you don’t have 4GB (232 bytes) of memory

## Slide 29: Example
Assume there are three small caches, each consisting of four one-word blocks. One cache is fully associative, a second is two-way set-associative, and the third is direct-mapped. Find the number of misses for each cache organization given the following sequence of block addresses: 0, 8, 0, 6, and 8.

## Slide 30: Solution: Direct Map

## Slide 31: Solution: Set Associative Cache

## Slide 32: Solution: Fully Associative

## Slide 36
Assume add is 4 clock cycles, multiply is 20 clock cycles, divide is 40 clock cycles and load is 4 clock cycles. Using the code segment below show the overall status tables when the ADD.D is ready to commit.

## Slide 38
Always 32 bits in MIPS
Size depends upon installed memory
32 bit program address space (4GB)
30 bit RAM address space (1GB)
0x00000000
0xFFFFFFFF
ADDRESS
Crash if we try to access more than 1GB
??

## Slide 39
How do programs share the memory
Where we do put them

## Slide 40
Program 2
(2GB)
Program 1
1GB
Program 3
(2GB)
32 bit RAM address space (4GB)

## Slide 41
Program 2
(2GB)
Program 1
1GB
Program 3
(2GB)
32 bit RAM address space (4GB)
Program 1 & 2 fit
(they use 3 GB of memory leaving 1GB free)

## Slide 42
Program 3
(2GB)
Program 1
Program 2
32 bit RAM address space (4GB)
Program 1 & 2 fit
(they use 3 GB of memory leaving 1GB free)

## Slide 43
Program 3
(2GB)
Program 2
32 bit RAM address space (4GB)
Quit program 1
Program 2 uses 2GB of memory leaving 2GB free
Program 1
1GB
1GB free
1GB free

## Slide 44
Program 3
(2GB)
Program 2
32 bit RAM address space (4GB)
Can’t run program 3
(even though we have enough space)
Memory Fragmentation
Program 1
1GB
1GB free
1GB free

## Slide 45
Each program can access any 32-bit memory address
What if multiple programm access the same address
  sw r2, 1024(r0) will write to the address 1024 regardless of the program that’s running
They can corrupt each other or crash each other
  Security & reliability

## Slide 46
Program 2
(2GB)
Program 1
1GB
10000
RAM address space
Address 1024

## Slide 47
Program 2
(2GB)
Program 1
1GB
310x000x
RAM address space
Address 1024
Program 1 stores the bank balance at address 1024
Program 2 stores the exam marks at address 1024
Program Address
1024
Program Address
1024

## Slide 48
If all programs have access to the same 32 bit memory space:
  Can crash if less than 4GB of RAM memory in the system
  Can run out of memory if we run multiple programs
  Can corrupt other program’s data

## Slide 49
How do we solve this
  Key to the problem “SAME MEMORY SPACE”
  Can we give each program its own virtual memory space
  If so we can
    Separately map each programs memory space to the RAM memory
    Mapping gives the flexibility in how we use the physical RAM

## Slide 50
Always 32 bits in MIPS
Size depends upon installed memory
32 bit program address space (4GB)
30 bit RAM address space (1GB)
0x00000000
0xFFFFFFFF
ADDRESS
Crash if we try to access more than 1GB
??

## Slide 51: Virtual Memory
VIRTUAL MEMORY takes program addresses and maps them to RAM addresses

## Slide 52
Always 32 bits in MIPS
Size depends upon installed memory
32 bit program address space (4GB)
30 bit RAM address space (1GB)
0x00000000
0xFFFFFFFF
ADDRESS
MAP

## Slide 53
Map some of the program’s address space to the disk
When we need it we bring it to the memory
Program 0
Program 1
Program2
Program 3
MAP
Program 1
Program 0
Program 2
Program loads address 0
VM maps address 0 to RAM1
Program loads address 1
VM maps address 1 to RAM 0
Program loads address 2
VM maps address 2 to RAM2
Program loads address 3
VM does not have any more space in RAM
Notes: Write the program address space and RAM address space

## Slide 54
Map some of the program’s address space to the disk
When we need it we bring it to the memory
Program 0
Program 1
Program2
Program 3
MAP
Program 1
Program 3
Program 2
Program loads address 0
Program loads address 1
Program loads address 2
Program loads address 3
VM moves oldest data (0) to Disk
VM updates the map to point data data 0 to disk
VM maps address 3 to RAM 1
Disk
Program 1
Notes: Write the program address space and RAM address space

## Slide 55
Mapping uses the secondary storage to give the illusion of unlimited memory

## Slide 56
How do we use the holes left when program quits
We can map a program address to RAM address however we like
Program 3
(2GB)
Program 2
32 bit RAM address space (4GB)
1GB free
1GB free
Program 2
(2GB)
Program 3 MAP
Program 2 MAP

## Slide 57
With virtual memory program addresses map to RAM addresses
Each program has its own mapping
Mapping can put program data where ever it wants in the RAM

## Slide 58
Program 2
(2GB)
Program 1
1GB
10000
0.0005
RAM address space
Program 1 stores the bank balance at address 1024
VM maps it to RAM address 3
Program 2 stores the exam marks at address 1024
VM maps it to RAM address 6
Security & Reliability
Program Address
1024
Program 1 MAP
Program Address
1024
Program 2 MAP
RAM Address
3
RAM Address
6

## Slide 59
Program 1’s & 2’s addresses map to different RAM addresses
Because each program has it’s own address space, they cannot access each other’s data

## Slide 60
Virtual Memory:
  What the program sees
    e.g. LDR r4, 1024(r0) accesses virtual address r0+1024=1024
Physical Memory:
  The physical RAM installed in the computer
    e.g. if there is 4GB of RAM installed you have physical addresses from 0 to 232 - 1

## Slide 61
Virtual address:
  what the program uses
  in MIPS, this is the full 32 bit address space (0 to 232-1)
Physical address:
  What the hardware uses to talk to the RAM
  Address space is determined by how much RAM is installed

## Slide 62
Program executes a load specifying a virtual address
Computer translates the address to the physical address in the memory
Data for r3
Data for r3
LDR r3, 1024(r0)
MAP | 
VA | PA
512 | 12
786 | Disk
1024 | 2
RAM
Physical address space
Program
Virtual address space
Translation
From VAPA
VA 1024
PA 2

## Slide 63
If the PA is not in the memory the OS loads it from disk
The computer then reads the RAM using the PA and returns the data to the program
Data for r3
Data for r3
LDR r3, 1024(r0)
LDR r2, 512 (r0)
ADD r4, r2, r3
LDR r5, 786(r0)
MAP | 
VA | PA
512 | 12
786 | Disk
1024 | 2
RAM
Physical address space
Program
Virtual address space
Translation
From VAPA
VA 786

## Slide 64
If the PA is not in the memory the OS loads it from disk
The computer then reads the RAM using the PA and returns the data to the program
Data for r3
Data for r5
Data for r3
LDR r3, 1024(r0)
LDR r2, 512 (r0)
ADD r4, r2, r3
LDR r5, 786(r0)
MAP | 
VA | PA
512 | 12
786 | Disk
1024 | 1
RAM
Physical address space
Program
Virtual address space
Translation
From VAPA
VA 786

## Slide 65
If the PA is not in the memory the OS loads it from disk
The computer then reads the RAM using the PA and returns the data to the program
Data for r3
Data for r5
Data for r3
LDR r3, 1024(r0)
LDR r2, 512 (r0)
ADD r4, r2, r3
LDR r5, 786(r0)
MAP | 
VA | PA
512 | 12
786 | 3
1024 | 1
RAM
Physical address space
Program
Virtual address space
Translation
From VAPA
VA 786
Update Translation MAP

## Slide 66
If the PA is not in the memory the OS loads it from disk
The computer then reads the RAM using the PA and returns the data to the program
Data for r3
Data for r5
Data for r3
LDR r3, 1024(r0)
LDR r2, 512 (r0)
ADD r4, r2, r3
LDR r5, 786(r0)
MAP | 
VA | PA
512 | 12
786 | 3
1024 | 1
RAM
Physical address space
Program
Virtual address space
Translation
From VAPA
VA 786
Update Translation MAP

## Slide 67
The map from VA to PA address is called Page table
So far one page table entry for every VA
How many entries for 32 bit virtual address??
1 for every byte = 232 (4 billion)
1 for every word= 230 (1 billion)

## Slide 68
If we don’t have a page table entry we cannot access them because we cannot find the physical address
How can we make it more manageable
  What if we divided memory up into chunks (pages) instead of words

## Slide 69
MAP | 
VA | PA
512 | 12
786 | Disk
1024 | 2
MAP | 
VA | PA
0-4096 | 8192-4096
MAP
Translates from VAPA
MAP
Translates from VAPA
FINE GRAIN:
MAPS each word address
230 words to map
COURSE GRAIN:
MAPS chunks of addresses Fewer mappings
4KB pages
Each entry now covers 4KB of data
Notes: Exaplaination:

## Slide 70
The page table maps larger chunks (pages) of data
  Fewer page table entries needed to cover the whole address space
  Less flexible
  Typically 4KB pages
  Sometimes 2MB pages

## Slide 71
MAP | 
VA | PA
0-4096 | 4096-8191
COURSE GRAIN:
MAPS chunks of addresses Fewer mappings
MAP
Translates from VAPA
4KB pages
Each entry now covers 4KB of data

## Slide 72
Virtual Address Space | 
16382 12280 | 
12287 8192 | 
8191 4096 | 
4095 0 | 
12287 8192 | 
8191 4096 | 
4095 0 | 
Physical Address
Space
What is the physical address for virtual address 4

## Slide 73
Virtual Address Space | 
16382 12280 | 4KB
12287 8192 | 4KB
8191 4096 | 4KB
4095 0 | 4KB
12287 8192 | 4KB
8191 4096 | 4KB
4095 0 | 4KB
Physical Address
Space
VA is 4 bytes offset from the start of virtual page at VA 0
It will map to 4 bytes offset from corresponding physical page:
4096+4

## Slide 74
What happens on a 32 bit machine with 256 MB of RAM and 4 KB pages
20 bits | 12 bits
16 bits | 12 bits
Page table
Each PTE handles 4KB of address space
For each page we have 4096 addresses (12) bits that don’t get translated
Virtual Page No.
Physical Page No.
Page Offset.
Page Offset.
Virtual Address
Physical Address

## Slide 75
What happens on a 32 bit machine with 256 MB of RAM and 4 KB pages
20 bits | 12 bits
16 bits | 12 bits
Page table
Each PTE handles 4KB of address space
For each page we have 4096 addresses (12) bits that don’t get translated
Virtual Page No.
Physical Page No.
Page Offset.
Page Offset.
Virtual Address
Physical Address
4095 0 | 4KB
8191 4096 | 4KB

## Slide 76
Virtual Address Space | 
16382 Virtual Page No. 3 12280 | 4KB
12287 Virtual Page No. 2 8192 | 4KB
8191 Virtual Page No. 1 4096 | 4KB
4095 Virtual Page No. 0 0 | 4KB
12287 8192 | 4KB
8191 4096 | 4KB
4095 0 | 4KB
Physical Address
Space
20 bits | 12 bits
16 bits | 12 bits
Which Page
Page Offset
Which Page
Page Offset
Virtual Address Space
232-1
Physical Address Space
TRANSLATION

## Slide 77
20 bits | 12 bits
 | Physical Page No.
0x00000 | Disk
0x00001 | 0x0003
0x00002 | 0x0005
0xfffff | 0x00f6
16 bits | 12 bits
Virtual Page No.
Physical Page No.
Page Offset.
Page Offset.
Virtual Address
Physical Address
Page Table Entry (PTE) tells which page
4KB page =12 bits for page offset
Same for VA & PA
No translation
Virtual Address (VA) size set by ISA
Physical Address (PA) size set by amount of RAM

## Slide 78
20 bits | 12 bits
 | Physical Page No.
0x00000 | Disk
0x00001 | 0x0003
0x00002 | 0x0005
0xfffff | 0x00f6
16 bits | 12 bits
Virtual Page No.
Physical Page No.
Page Offset.
Page Offset.
Virtual Address
Physical Address

## Slide 79
20 bits | 12 bits
 | Physical Page No.
0x00000 | Disk
0x00001 | 0x0003
0x00002 | 0x0005
0xfffff | 0x00f6
16 bits | 12 bits
Virtual Page No.
Physical Page No.
Page Offset.
Page Offset.
Virtual Address
Physical Address

## Slide 83: TLB
20 bits | 12 bits
 | Physical Page No.
0x00000 | Disk
0x00001 | 0x0003
0x00002 | 0x0005
0xfffff | 0x00f6
16 bits | 12 bits
Virtual Page No.
Physical Page No.
Page Offset.
Page Offset.
Virtual Address
Physical Address