## Slide 1: Caches-II
Dr. Farhan Hussain

## Slide 2: Handling Cache Misses
Cache Miss
  A request for data from the cache that cannot be filled because the data is not present in the cache.
Steps to be taken on an instruction cache miss:
  Send the original PC value (current PC – 4) to the memory.
  Instruct main memory to perform a read and wait for the memory to complete its access.
  Write the cache entry, putting the data from memory in the data portion of the entry, writing the upper bits of the address (from the ALU) into the tag field, and turning the valid bit on.
  Restart the instruction execution at the first step, which will re-fetch the instruction, this time finding it in the cache.

## Slide 3: Handling Writes
write-through
  A scheme in which writes always update both the cache and the next lower level of the memory hierarchy, ensuring that data is always consistent between the two.
  For example, suppose 10% of the instructions are stores. If the CPI without cache misses was 1.0, spending 100 extra cycles on every write would lead to a CPI of 1.0 + 100 × 10% = 11, reducing performance by more than a factor of 10.
write buffer
  A queue that holds data while the data is waiting to be written to memory.

## Slide 4: Handling Writes
write-back
  A scheme that handles writes by updating values only to the block in the cache, then writing the modified block to the lower level of the hierarchy when the block is replaced.

## Slide 5: An Example Cache: The Intrinsity FastMATH Processor

## Slide 6: Four-way set-associative Cache

## Slide 7: One-word-wide Memory Organization
1 memory bus clock cycle to send the address
15 memory bus clock cycles for each DRAM access initiated
1 memory bus clock cycle to send a word of data

## Slide 8: Wider memory organization
1 memory bus clock cycle to send the address
15 memory bus clock cycles for each DRAM access initiated
1 memory bus clock cycle to send a word of data

## Slide 9: Interleaved memory organization
1 memory bus clock cycle to send the address
15 memory bus clock cycles for each DRAM access initiated
1 memory bus clock cycle to send a word of data

## Slide 10: Measuring and Improving Cache Performance
CPU time = (CPU execution clock cycles + Memory-stall clock cycles) × Clock cycle time
Memory-stall clock cycles = Read-stall cycles + Write-stall cycles
Read-stall cycles = Reads /Program ×Read miss rate × Read miss penalty
Write-stall cycles = ( Writes/Program × Write miss rate × Write miss penalty ) + Write buffer stalls

## Slide 11: Measuring and Improving Cache Performance
Memory-stall clock cycles = Memory accesses/ Program × Miss rate × Miss penalty
We can also factor this as:
Memory-stall clock cycles = Instructions/ Program × Misses/Instruction × Miss penalty

## Slide 12: Calculating Cache Performance
Assume the miss rate of an instruction cache is 2% and the miss rate of the data cache is 4%. If a processor has a CPI of 2 without any memory stalls and the miss penalty is 100 cycles for all misses, determine how much faster a processor would run with a perfect cache that never missed. Assume the frequency of all loads and stores is 36%.

## Slide 13: Calculating Cache Performance
The number of memory miss cycles for instructions in terms of the Instruction count (I) is
Instruction miss cycles = I × 2% × 100 = 2.00 × I
As the frequency of all loads and stores is 36%, we can find the number of memory miss cycles for data references:
Data miss cycles = I × 36% × 4% × 100 = 1.44 × I
The total number of memory-stall cycles is 2.00 × I + 1.44 × I = 3.44 × I. This is more than three cycles of memory stall per instruction. Accordingly, the total CPI including memory stalls is 2 + 3.44 = 5.44. Since there is no change in instruction count or clock rate, the ratio of the CPU execution times is:
CPU time with stalls / CPU time with perfect cache =
(I × CPIstall × Clock cycle)/(I × CPIperfect × Clock cycle) = CPIstall / CPIperfect = 5.44/2
The performance with the perfect cache is better by 5.44/2 = 2.72.

## Slide 14: Calculating Cache Performance
Suppose we speed-up the computer in the previous example by reducing its CPI from 2 to 1without changing the clock rate, which might be done with an improved pipeline then:

## Slide 15: Average Memory Access Time (AMAT)
Average memory access time is the average time to access memory considering both hits and misses and the frequency of different accesses; it is equal to the following:
AMAT = Time for a hit + Miss rate × Miss penalty

## Slide 16: Average Memory Access Time (AMAT)
Find the AMAT for a processor with a 1 ns clock cycle time, a miss penalty of 20 clock cycles, a miss rate of 0.05 misses per instruction, and a cache access time (including hit detection) of 1 clock cycle. Assume that the read and write miss penalties are the same and ignore other write stalls.
The average memory access time per instruction is
AMAT = Time for a hit + Miss rate × Miss penalty
= 1 + 0.05 × 20
= 2 clock cycles or 2 ns.

## Slide 17: Cache Replacement
Miss : need to put a new block in the cache. Which block do we kick out ?
    Random
    FIFO
    LRU
      NMRU
      PLRU

## Slide 18: Implementing the LRU
References: A, B, C, D, E, B, B, D & B
Data | Tag | Valid | LRU
 |  |  | 0
 |  |  | 1
 |  |  | 2
 |  |  | 3

## Slide 19: Implementing the LRU
References: A, B, A, D, K
Data | Rank
A | 7
B | 3
C | 2
D | 6
E | 5
F | 1
G | 4
H | 0

## Slide 20: Write Policy
Write allocate
  Allocate a block in the cache for writing
No write allocate
  Do not allocate a block in cache for writing
Write through cache
  Update cache immediately
Write back caches
  Update cache on replacement
    Dirty bit can be “0 ” or “1”

## Slide 21: Write Back cache
Write A, Read A, Read B, Read C, Write C, Read D, Read F
Valid Bit | Tag | Dirty Bit | Data
0 |  |  | 
0 |  |  | 
0 |  |  | 

## Slide 22: Write back Cache (Q)
Suppose a cache with only one line :
  Read A, Read B, Write B, Read C, Read D, Write D
  How many misses we have ?
  How many write backs we have ?
Valid Bit | Dirty Bit | Tag | Data
0 | 1 | Tag of M | M

## Slide 23: Way Prediction
 | 32 KB and 8 way set associative cache | 4KB direct mapped cache | 32 KB and 8 way set associative cache with way prediction
Hit Rate | 90% | 70% | 90%
Hit Latency | 2 | 1 | 1 or 2
Miss penalty | 20 | 20 | 20
AMAT |  |  | 

## Slide 24: Way Prediction
 | 32 KB and 8 way set associative cache | 4KB direct mapped cache | 32 KB and 8 way set associative cache with way prediction
Hit Rate | 90% | 70% | 90%
Hit Latency | 2 | 1 | 1 or 2
Miss penalty | 20 | 20 | 20
AMAT | 2+0.1 * 20 | 1+0.3*20 | 0.7*1+0.3*2+0.1*20

## Slide 25: Cache Replacement
Miss : need to put a new block in the cache. Which block do we kick out ?
    Random
    FIFO
    LRU
      NMRU
      PLRU

## Slide 26: Not Most Recently Used
Fully associative cache with 04 lines
Empty at the start
Accesses: A, A, B, A, C, A, D, A, E, A, A,A,A, B

## Slide 27: Multi-Level Caches
AMAT for Multilevel Cache:

## Slide 28: Multi-Level Cache Performance
A
 | 16 KB | 128 KB | No Cache | L1=16 KB L2=128 KB
Hit Rate | 90% | 97.5% | 100 | 90% for L1 75% for L2
Hit Latency | 2 | 10 | 100 | 02 for L1 12 for L2
Miss penalty | 20 | 20 | 100 | 20
AMAT |  |  |  | 

## Slide 29: Multi-Level Cache Performance
A
 | 16 KB | 128 KB | No Cache | L1=16 KB L2=128 KB
Hit Rate | 90% | 97.5% | 100 | 90% for L1 75% for L2
Hit Latency | 2 | 10 | 100 | 02 for L1 12 for L2
Miss penalty | 20 | 20 | 100 | 20
AMAT | 2+0.1×100=12 | 10+0.025×100=12.5 | 100 | 2+0.1×(10+0.25×100)=5.5