## Slide 1: REORDER BUFFERS

## Slide 2: Steps when an Exception Occurs
Save the address of the instruction generating the exception
Jump to the exception handler
Exception handler should come back at the instruction generating the exception
The program execution should begin from the instruction that generated the exception

## Slide 3: Exception in Out-of Order Execution
 | Instruction | IS | DIS | WR
1 | DIV F10, F0, F6 | 1 | 2 | 42
2 | LD F2, 45(R3) | 2 | 3 | 13
3 | MUL F0, F2,F4 | 3 | 14 | 19
4 | SUB F8, F2, F6 | 4 | 14 | 15
Let’s suppose F6=0 (divide by 0) detected in cycle 40 some where towards the end of the divide
*

## Slide 4: Problem
In cycle 40 we have already executed the 3 instructions (i.e. LD, MUL, SUB) following the divide and written their result.
If we go to the exception handler and come back the DIV it will use the F0 produced by the MUL.
Never going to get the correct result.
A major disadvantage of Tomasulo’s algorithm

## Slide 5: Branch Misprediction in OoO Execution
DIV R1, R3, R4
BEQ R1, R2, LABEL
ADD R3, R4,R5
This branch can be predicted, but it takes a very long time to realize it is mispredicted

## Slide 6: Problem
Let’s suppose we have made a prediction (i.e. not taken) and fetched the ADD instruction, executed it and written the result R3
After 40 cycles or so we realize that it was a misprediction
The ideal behaviour would be that we have never executed the ADD instruction and instead start fetching instructions from the label the branch is pointing to
Impossible because R3 by that time has already been updated

## Slide 7: Problem
Instead of having the old value of R3 we have the new value of R3 when we jump to the label
  A problem very much similar to the exception’s one.

## Slide 8: False Exception
DIV R1, R3, R4
BEQ R1, R2, LABEL
ADD R3, R4,R5
------------------------------------------------ ------------------------------------------------
LABEL: DIV R6, R7, R8
Let us suppose the DIV generates an exception (Exception handling occurs)…..even this instruction was never supposed to be executed but we have already started exception processing for it.

## Slide 9: Problem
An instruction can complete and write to register before the preceding instructions have fully been verified, and before we know that this instruction should have been executed

## Slide 10: Correct OoO Execution
Execution OoO
Broadcast OoO
But deposit values to register in order.

## Slide 11: Solution: Reorder Buffer
Remember program order
Keeps result of instructions until they are safe to write to registers
  Instead of writing to the registers directly we end up writing in the reorder buffer
  After writing into the reorder buffer we will deposit the results into the registers in order.
  Once the result are written to the registers through the reorder buffer they are considered as fully done

## Slide 12: Reorder Buffer
REG | VAL | DONE
We need reorder buffer to hold the results of the instructions until they are ready to finish in program order
REG
VAL
DONE

## Slide 13: Reorder Buffer
REG | VAL | DONE
COMMIT
Pointer
ISSUE
Pointer
Valid Instructions

## Slide 14: Reorder Buffer
Get a free reservation station
Get a reorder buffer entry
  Different from reservation station: get any entry that is free
  For ROB: need to get the entry that is next to the issue pointer
  The issue pointer will move and point to the next entry in the reorder buffer
Point the RAT entry to the ROB entry instead of reservation station

## Slide 15: Reorder Buffer
 |  | REG | VAL | DONE
Commit | 0 |  |  | 
 | 1 |  |  | 
Issue | 2 |  |  | 
 | 3 |  |  | 
 | 4 |  |  | 
RAT
REG
Reservation Station |  | 
ADD
IQ
R1=R2+R3

## Slide 16: Reorder Buffer
 |  | REG | VAL | DONE
Commit | 0 |  |  | 
 | 1 |  |  | 
 | 2 | R1 |  | 0
Issue | 3 |  |  | 
 | 4 |  |  | 
RAT | 
0 | 
1 | ROB2
2 | 
3 | 
REG
Reservation Station |  | 
ADD | ~~~~~~ | ~~~~~~
ADD
IQ

## Slide 17: Reorder Buffer
Issue
Execute
Broadcast with the tag of reorder buffer to the ROB and all reservation stations
  Previously it was with the tag of RS
  Note that we have already freed the RS

## Slide 18: Reorder Buffer
Commit
  With out the reorder buffer we would capture the result in the register file and update the RAT to point to that register
  With ROB we don’t want to write to the register yet so we write to the ROB instead
  Mark the instruction as done
  The result of the instruction isn’t going to the register file yet so we do not update the RAT to point to the register file. In fact the RAT is still pointing to the correct place.
  The instruction is marked as complete but we have not deposited the result in the register

## Slide 19: Reorder Buffer
To Commit this result:
  We should commit all of the previous instructions
  In each cycle we check whether the next instruction after the commit point is done if it is done we move the commit pointer and commit the instruction
  Result would be written to the register
  RAT must be updated because the ROB entry is freed after commit

## Slide 20: Reorder Buffer
Dispatch as soon as the operands are ready, execute and broadcast the result with the tag of ROB6 (Similar to Tomosula’s algorithm
FREEING OF RESERVATION STATION
AS SOON AS THE INSTRUCTION IS DISPATCHED

## Slide 21: Reorder Buffer
Updating the RAT has moved from the broadcast time to the commit time.

## Slide 22: Reorder Buffer
 |  | REG | VAL | DONE
Commit | 0 |  |  | 
 | 1 |  |  | 
Issue | 2 |  |  | 
 | 3 |  |  | 
 | 4 |  |  | 
RAT
REG
Reservation Station |  | 
ADD
IQ
R1=R2+R3

## Slide 23: Reorder Buffer
 |  | REG | VAL | DONE
Commit | 0 |  |  | 
 | 1 |  |  | 
 | 2 | R1 |  | 0
Issue | 3 |  |  | 
 | 4 |  |  | 
RAT | 
0 | 
1 | ROB2
2 | 
3 | 
REG
Reservation Station |  | 
ADD | ~~~~~~ | ~~~~~~
ADD
IQ

## Slide 24
Dispatch as soon as the operands are ready, execute and broadcast the result wit the tag of ROB6 (Similar to Tomosula’s algorithm
FREEING OF RESERVATION STATION
AS SOON AS THE INSTRUCTION IS DISPATCHED

## Slide 25
 |  | REG | VAL | DONE
Commit | 0 |  |  | 
 | 1 |  |  | 
 | 2 | R1 | 15 | 1
Issue | 3 |  |  | 
 | 4 |  |  | 
RAT | 
0 | 
1 | ROB2
2 | 
3 | 
REG
Reservation Station |  | 
FREE |  | 
ADD
IQ

## Slide 26
 |  | REG | VAL | DONE
 | 0 |  |  | 
 | 1 |  |  | 
Commit | 2 | R1 | 15 | 1
Issue | 3 |  |  | 
 | 4 |  |  | 
RAT | 
0 | 
1 | R1
2 | 
3 | 
REG
15
Reservation Station |  | 
FREE |  | 
ADD
IQ

## Slide 27: Summary
ISSUE:
  Reserve a reservation station
  Reserve a ROB entry
  Point RAT to ROB entry
Exec
  Read
  Send to exec unit
  Free RS

## Slide 28: Summary
Broadcast:
  Capture the results
    Reorder buffer
    Reservation stations
  Write to reorder buffer
  Update RAT
Commit:
  Write to registers
  Update RAT

## Slide 29: Branch Misprediction Recovery
LD R1, 0(R1)
BNE R2, R1, R1
ADD R2, R1, R1
MUL R3, R3, R4
DIV R2, R3, R7
Suppose our prediction was that the program will continue here and fetch the three instructions
Although in fact the program branches but still the three instructions would be executed

## Slide 30: Branch Misprediction Recovery
REG
RAT
 | REG | VAL | DONE
Commit |  |  | 
Issue |  |  | 

## Slide 31: Branch Misprediction Recovery
REG
RAT
ROB1
 | REG | VAL | DONE
Commit |  |  | 
 | R1 |  | 0
Issue |  |  | 

## Slide 32: Branch Misprediction Recovery
REG
RAT
ROB1
 | REG | VAL | DONE
Commit |  |  | 
 | R1 |  | 0
 |  |  | 0
Issue |  |  | 

## Slide 33: Branch Misprediction Recovery
REG
RAT
ROB1
ROB3
 | REG | VAL | DONE
Commit |  |  | 
 | R1 |  | 0
 |  |  | 0
 | R2 |  | 0
Issue |  |  | 

## Slide 34: Branch Misprediction Recovery
REG
RAT
ROB1
ROB3
ROB4
 | REG | VAL | DONE
Commit |  |  | 
 | R1 |  | 0
 |  |  | 0
 | R2 |  | 0
 | R3 |  | 0
Issue |  |  | 

## Slide 35: Branch Misprediction Recovery
REG
RAT
ROB1
ROB3/ ROB5
ROB4
 | REG | VAL | DONE
Commit |  |  | 
 | R1 |  | 0
 |  |  | 0
 | R2 |  | 0
 | R3 |  | 0
 | R2 |  | 0
Issue |  |  | 

## Slide 36
Suppose
  Load takes a long time to execute
  Branch depends upon the load so we can not sort out instead we predict
  Add also co-depends on the load and cannot complete
  Multiply can begin because independent
    Lets suppose multiply produces a value of 10
    Originally we would write it to the registers but now we would write to the ROB
How to undo the multiplication after we have discovered that the branch is mispredicted

## Slide 37: Branch Misprediction Recovery
REG
RAT
ROB1
ROB3/ ROB5
ROB4
 | REG | VAL | DONE
Commit |  |  | 
 | R1 |  | 0
 |  |  | 0
 | R2 |  | 0
 | R3 | 15 | 1
 | R2 |  | 0
Issue |  |  | 

## Slide 38: Branch Misprediction Recovery
REG
RAT
ROB1
ROB3/ ROB5
ROB4
 | REG | VAL | DONE
Commit |  |  | 
 | R1 |  | 0
 |  |  | 0
 | R2 |  | 0
 | R3 | 15 | 1
 | R2 | 5 | 1
Issue |  |  | 

## Slide 39: Branch Misprediction Recovery
So Multiply and Divide have been completed
We only updated the reorder buffer. The registers are still unmodified
Eventually the load would complete and marked as done

## Slide 40: Branch Misprediction Recovery
REG
RAT
ROB1
ROB3/ ROB5
ROB4
 | REG | VAL | DONE
Commit |  |  | 
 | R1 | 100 | 1
 |  |  | 0
 | R2 |  | 0
 | R3 | 15 | 1
 | R2 | 5 | 1
Issue |  |  | 

## Slide 41: Branch Misprediction Recovery
We can proceed to the branch test
We check whether we can commit the first instruction or not
  Can be committed why?

## Slide 42: Branch Misprediction Recovery
REG
100
RAT
ROB1
ROB3/ ROB5
ROB4
 | REG | VAL | DONE
Commit | R1 | 100 | 1
 |  |  | 0
 | R2 |  | 0
 | R3 | 15 | 1
 | R2 | 5 | 1
Issue |  |  | 

## Slide 43: Branch Misprediction Recovery
Suppose that the branch takes longer to figure out than the ADD, so the ADD completes before the establishment of the branch

## Slide 44: Branch Misprediction Recovery
REG
100
RAT
ROB1
ROB3/ ROB5
ROB4
 | REG | VAL | DONE
Commit | R1 | 100 | 1
 |  |  | 0
 | R2 | 8 | 1
 | R3 | 15 | 1
 | R2 | 5 | 1
Issue |  |  | 

## Slide 45: Branch Misprediction Recovery
Eventually the branch is resolved and it has been figured out that it has been predicted and we can start fetching from the correct instructions
How to get rid of those that we have done wrong
  We mark the branch that it is a misprediction
  At the point where the commit has reached, the registers contain exactly the values we need (i.e upto the point of the branch)
  All of the instructions prior to the branch have been committed which means that their updates have been reflected in the registers
  None of the instructions after the branch have updated the registers

## Slide 46: Branch Misprediction Recovery
REG
100
RAT
ROB3/ ROB5
ROB4
 | REG | VAL | DONE
Commit |  | ! | 1
 | R2 | 8 | 1
 | R3 | 15 | 1
 | R2 | 5 | 1
Issue |  |  | 

## Slide 47: Branch Misprediction Recovery
Reversing : (1)empty the ROB
  After the branch is committed we make the ROB empty by simply putting the issue pointer in the same place
    Issune new instructions and mark them as undone
(2): RAT contains the wrong values: Simply make the RAT to point to the register file
Emptying out what ever is left in reservation stations and the ALU
  Basically free all the reservation station and stop ALU from broadcasting results in the future

## Slide 48: Branch Misprediction Recovery
REG
100
RAT
 | REG | VAL | DONE
Commit Issue |  | ! | 1
Issue |  |  | 

## Slide 49: Branch Misprediction Recovery
It looks like these instruction have never been executed or issued
  We are able to undo the damage

## Slide 50: Branch Misprediction Recovery
RECOVERY
  ROB  Empty
  RAT  REG
  RS, ALU  Empty

## Slide 51: Exceptions
Divide by ‘0’
DIV R0, R1, R2
ADD R2, R5, R4

## Slide 52: Page Fault for loads

## Slide 53: False Exceptions
The result is going to be marked as an exception
  Because we haven't committed anything yet we just cancel the instructions that generated the false exception
BEQ R1, R2, Label
DIV R0, R0, R5

## Slide 54
Delay the handling of the exceptions until the instruction that is triggering the exception commits

## Slide 55: Insight
ADD R1, R2, R3
BNE R1, R3, label
DIV R7, R8, R9
………….
………….
Label: MUL R5, R6, R7

## Slide 56
What the programmer sees and what’s the real state of the processor

## Slide 57: RAT update on Commit
REG
RAT
ROB4 (R1)
**ROB5 (R2)
**ROB2 (R3)
 | REG | VAL | DONE
*ROB1 | R1 | R2+R3 | 1
ROB2 | R3 | R5+R6 | 1
ROB3 | R1 | ROB1+R7 | 1
ROB4 | R1 | R4+R8 | 1
ROB5 | R2 | R9+ROB2 | 1
Let us suppose that all of these instructions have finished and put their results in the ROB and now its time to commit them (* is the next instruction to be committed)
Register allocation table
Register File
--This entry (ROB4) is the latest one to write to R1

## Slide 58: RAT update on Commit
-- originally it was pointing to the REG then made to point to the ROB1, then to ROB3 and then finally to ROB4
** the latest rename to R2
** the latest rename to R3

## Slide 59
Now we will commit in the correct order (in order of program execution)
Each time we are going to commit an instruction we will deposit its result in the registers no matter what the RAT really says.
However we are going to check whether we are the latest rename and if we are not we are not going to change the RAT
  But if we are then we are going to change the RAT

## Slide 60: RAT update on Commit
REG
*R2+R3
RAT
ROB4 (R1)
ROB5 (R2)
ROB2 (R3)
 | REG | VAL | DONE
ROB1 | R1 | R2+R3 | 1
ROB2 | R3 | R5+R6 | 1
ROB3 | R1 | ROB1+R7 | 1
ROB4 | R1 | R4+R8 | 1
ROB5 | R2 | R9+ROB2 | 1
Even though the naming in RAT says that this* is not the latest value for the register

## Slide 61: RAT update on Commit
REG
*R2+R3
RAT
ROB4 (R1)
ROB5 (R2)
ROB2 (R3)
 | REG | VAL | DONE
ROB1 | R1 | R2+R3 | 1
ROB2 | R3 | R5+R6 | 1
ROB3 | R1 | ROB1+R7 | 1
ROB4 | R1 | R4+R8 | 1
ROB5 | R2 | R9+ROB2 | 1
Even though the naming in RAT says that this* is not the latest value for the register

## Slide 62: RAT update on Commit
REG
R2+R3
RAT
ROB4 (R1)
ROB5 (R2)
ROB2 (R3)
 | REG | VAL | DONE
ROB2 | R3 | R5+R6 | 1
ROB3 | R1 | ROB1+R7 | 1
ROB4 | R1 | R4+R8 | 1
ROB5 | R2 | R9+ROB2 | 1

## Slide 63: RAT update on Commit
REG
R2+R3
R5+R6
RAT
ROB4 (R1)
ROB5 (R2)
ROB2 (R3)
 | REG | VAL | DONE
ROB2 | R3 | R5+R6 | 1
ROB3 | R1 | ROB1+R7 | 1
ROB4 | R1 | R4+R8 | 1
ROB5 | R2 | R9+ROB2 | 1
As we are the latest rename for this value we are going to make the RAT point to REG file. If we do not do it, because we are freeing the ROB2, the RAT would be pointing to an empty location

## Slide 64: RAT update on Commit
REG
R2+R3
R5+R6
RAT
ROB4 (R1)
ROB5 (R2)
 | REG | VAL | DONE
ROB3 | R1 | ROB1+R7 | 1
ROB4 | R1 | R4+R8 | 1
ROB5 | R2 | R9+ROB2 | 1
So basically now if any instruction wants to access R3, it actually needs to get the value from the register file and not the ROB
After we have committed we can just free this ROB entry

## Slide 65: RAT update on Commit
REG
R2+R3 ROB1+R7
R5+R6
RAT
ROB4 (R1)
ROB5 (R2)
 | REG | VAL | DONE
ROB3 | R1 | ROB1+R7 | 1
ROB4 | R1 | R4+R8 | 1
ROB5 | R2 | R9+ROB2 | 1

## Slide 66: RAT update on Commit
REG
R2+R3 ROB1+R7
R5+R6
RAT
ROB4 (R1)
ROB5 (R2)
 | REG | VAL | DONE
ROB4 | R1 | R4+R8 | 1
ROB5 | R2 | R9+ROB2 | 1

## Slide 67
Why do we do this????

## Slide 68: RAT update on Commit
REG
R2+R3 ROB1+R7 R4+R8
R5+R6
RAT
ROB4 (R1)
ROB5 (R2)
 | REG | VAL | DONE
ROB4 | R1 | R4+R8 | 1
ROB5 | R2 | R9+ROB2 | 1

## Slide 69: RAT update on Commit
REG
R2+R3 ROB1+R7 R4+R8
R5+R6
RAT
ROB5 (R2)
 | REG | VAL | DONE
ROB5 | R2 | R9+ROB2 | 1

## Slide 70: RAT update on Commit
REG
R2+R3 ROB1+R7 R4+R8
R9+ROB2
R5+R6
RAT
ROB5 (R2)
 | REG | VAL | DONE
ROB5 | R2 | R9+ROB2 | 1

## Slide 71: RAT update on Commit
REG
R2+R3 ROB1+R7 R4+R8
R9+ROB2
R5+R6
RAT
 | REG | VAL | DONE

## Slide 72
 | Inst | Operands
1 | DIV | R2, R3, R4
2 | MUL | R1, R5, R6
3 | ADD | R3, R7, R8
4 | MUL | R1, R1, R3
5 | SUB | R4, R1,R5
6 | ADD | R1, R4, R2
ADD | 1 CYCLE
MULT | 10 CYCLES
DIV | 40 CYCLES

## Slide 73
DIV | ROB1 |  |  | 45 | 5
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | 
R2 | ROB1
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 |  |  |  | 
ROB3 |  |  |  | 
ROB4 |  |  |  | 
ROB5 |  |  |  | 
ROB6 |  |  |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 |  |  | 

## Slide 74
MUL | ROB2 |  |  | 3 | 4
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB2
R2 | ROB1
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 |  | 
ROB3 |  |  |  | 
ROB4 |  |  |  | 
ROB5 |  |  |  | 
ROB6 |  |  |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 |  |  | 

## Slide 75
ADD | ROB3 |  |  | 1 | 2
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB2
R2 | ROB1
R3 | ROB3
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 |  | 
ROB3 | ADD | R3 |  | 
ROB4 |  |  |  | 
ROB5 |  |  |  | 
ROB6 |  |  |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 | 3 |  | 
3 |  |  | 

## Slide 76
MUL | ROB4 | ROB2 | ROB3 |  | 
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB4
R2 | ROB1
R3 | ROB3
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 |  | 
ROB3 | ADD | R3 |  | 
ROB4 | MUL | R1 |  | 
ROB5 |  |  |  | 
ROB6 |  |  |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 | 3 |  | 
3 | 4 |  | 
4 |  |  | 

## Slide 77
SUB | ROB5 | ROB4 |  |  | 3
MUL | ROB4 | ROB2 |  |  | 3
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB4
R2 | ROB1
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 |  | 
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 |  | 
ROB5 | SUB | R4 |  | 
ROB6 |  |  |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 | 3 |  | 
3 | 4 | 5 | 
4 |  |  | 
5 |  |  | 

## Slide 78
SUB | ROB5 | ROB4 |  |  | 03
ADD | ROB6 | ROB5 | ROB1 |  | 
MUL | ROB4 | ROB2 |  |  | 03
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | ROB1
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 |  | 
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 |  | 
ROB5 | SUB | R4 |  | 
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 | 3 |  | 
3 | 4 | 5 | 
4 |  |  | 
5 |  |  | 
6 |  |  | 

## Slide 79: _________________________
Although we have written the result of the ADD instruction we cannot commit it until all previous instructions have been committed.
In cycle 7 we have nothing to issue anymore we can not execute anything until we see any broad cast (and that happens in cycle 13)

## Slide 80
SUB | ROB5 | ROB4 |  |  | 03
ADD | ROB6 | ROB5 | ROB1 |  | 
MUL | ROB4 |  |  | 12 | 03
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | ROB1
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 |  | 
ROB5 | SUB | R4 |  | 
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 | 3 | 13 | 
3 | 4 | 5 | 
4 |  |  | 
5 |  |  | 
6 |  |  | 

## Slide 81
SUB | ROB5 | ROB4 |  |  | 03
ADD | ROB6 | ROB5 | ROB1 |  | 
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | ROB1
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 |  | 
ROB5 | SUB | R4 |  | 
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 | 3 | 13 | 
3 | 4 | 5 | 
4 | 14 |  | 
5 |  |  | 
6 |  |  | 

## Slide 82
SUB | ROB5 |  |  | 36 | 3
ADD | ROB6 | ROB5 | ROB1 |  | 
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | ROB1
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 |  | 
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 | 3 | 13 | 
3 | 4 | 5 | 
4 | 14 | 24 | 
5 |  |  | 
6 |  |  | 

## Slide 83
ADD | ROB6 | ROB5 | ROB1 |  | 
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | ROB1
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 |  | 
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 | 3 | 13 | 
3 | 4 | 5 | 
4 | 14 | 24 | 
5 | 25 |  | 
6 |  |  | 

## Slide 84
ADD | ROB6 |  | ROB1 | 33 | 
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | ROB1
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 |  | 
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 | 33 | 26D
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 |  | 
2 | 3 | 13 | 
3 | 4 | 5 | 
4 | 14 | 24 | 
5 | 25 | 26 | 
6 |  |  | 

## Slide 85
ADD | ROB6 |  |  | 33 | 9
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | ROB1
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 | 9 | 42D
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 | 33 | 26D
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 
2 | 3 | 13 | 
3 | 4 | 5 | 
4 | 14 | 24 | 
5 | 25 | 26 | 
6 |  |  | 

## Slide 86
ADD | ROB6 |  |  | 33 | 9
R1 | 23
R2 | 16
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | ROB1
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 | 9 | 42D
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 | 33 | 26D
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 
2 | 3 | 13 | 
3 | 4 | 5 | 
4 | 14 | 24 | 
5 | 25 | 26 | 
6 |  |  | 

## Slide 87
R1 | 23
R2 | 09
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | 
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 | 9 | 42D
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 | 33 | 26D
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 43
2 | 3 | 13 | 
3 | 4 | 5 | 
4 | 14 | 24 | 
5 | 25 | 26 | 
6 | 43 |  | 

## Slide 88
R1 | 23
R2 | 09
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | 
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 | 33 | 26D
ROB6 | ADD | R1 |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 43
2 | 3 | 13 | 
3 | 4 | 5 | 
4 | 14 | 24 | 
5 | 25 | 26 | 
6 | 43 |  | 

## Slide 89
R1 | 12
R2 | 09
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | 
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 | 33 | 26D
ROB6 | ADD | R1 | 42 | 44
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 43
2 | 3 | 13 | 44
3 | 4 | 5 | 
4 | 14 | 24 | 
5 | 25 | 26 | 
6 | 43 | 44 | 

## Slide 90
R1 | 12
R2 | 09
R3 | 45
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | 
R3 | ROB3
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 | 33 | 26D
ROB6 | ADD | R1 | 42 | 44
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 43
2 | 3 | 13 | 44
3 | 4 | 5 | 
4 | 14 | 24 | 
5 | 25 | 26 | 
6 | 43 | 44 | 

## Slide 91
R1 | 12
R2 | 09
R3 | 03
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | 
R3 | 
R4 | ROB5
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 | 9 | 42D
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 | 33 | 26D
ROB6 | ADD | R1 | 42 | 44
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 43
2 | 3 | 13 | 44
3 | 4 | 5 | 45
4 | 14 | 24 | 
5 | 25 | 26 | 
6 | 43 | 44 | 

## Slide 92
R1 | 36
R2 | 09
R3 | 03
R4 | 05
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | ROB6
R2 | 
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 | 9 | 42D
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB4 | MUL | R1 | 36 | 24D
ROB5 | SUB | R4 | 33 | 26D
ROB6 | ADD | R1 | 42 | 44
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 43
2 | 3 | 13 | 44
3 | 4 | 5 | 45
4 | 14 | 24 | 46
5 | 25 | 26 | 
6 | 43 | 44 | 

## Slide 93
R1 | 36
R2 | 09
R3 | 03
R4 | 33
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | 
R2 | 
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 | 9 | 42D
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB5 | SUB | R4 | 33 | 26D
ROB6 |  |  |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 43
2 | 3 | 13 | 44
3 | 4 | 5 | 45
4 | 14 | 24 | 46
5 | 25 | 26 | 47
6 | 43 | 44 | 

## Slide 94
R1 | 42
R2 | 09
R3 | 03
R4 | 33
R5 | 03
R6 | 04
R7 | 01
R8 | 02
R1 | 
R2 | 
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R0B1 | DIV | R2 | 9 | 42D
ROB2 | MUL | R1 | 12 | 13D
ROB3 | ADD | R3 | 3 | 5 D
ROB5 | SUB | R4 | 33 | 26D
ROB6 |  |  |  | 
ROB7 |  |  |  | 
ROB8 |  |  |  | 
1 | 2 | 42 | 43
2 | 3 | 13 | 44
3 | 4 | 5 | 45
4 | 14 | 24 | 46
5 | 25 | 26 | 47
6 | 43 | 44 | 48